## Slide 1: ICS第四次小班课 10.29
Processor Arch:
ISA & Logic Sequential
MADE BY: Zhong Zhineng & You Zhenbang
TA：Wenhao Tang

## Slide 2
Processor Arch: ISA

## Slide 3
ISA
“The ISA serves as the boundary between the software and hardware.”
—— Computer Architecture: A Quantitative Approach
Instruction set architecture is the structure of a computer that a machine language programmer (or a compiler) must understand to write a correct (timing independent) program for that machine.
—— IBM introducing 360 (1964)

## Slide 4
ISA
1964，Amdahl、Blaauw和Brooks 在Architecture of the IBM system 360一文中，给出了“体系结构”的定义：
The term architecture is used here to describe the attributes of a system as seen by the programmer, i.e., the conceptual structure and functional behavior, as distinct from the organization of the data flow and controls, the logical design, and the physical implementation.
ISA包括各种状态单元、指令集和他们的编码、一组编程规范和异常事件处理

## Slide 5
ISA

## Slide 6
ISA

## Slide 7
Y86-64 Programmer-Visible State
Program Registers
Memory
Condition Codes
Program Status
Program Counter

## Slide 8
Y86-64 Instruction Set & Encoding
Instruction Code
Function Code
Immediate

## Slide 9
RISC vs. CISC
Examples
  CISC
    x86
  RISC
    ARM
    RISC-V
    MIPS

## Slide 10
RISC vs. CISC
CISC | RISC
Multiple formats for specifying operands. | Simple addressing formats.
Arithmetic and logical operations can be applied to both memory and register operands. | Arithmetic and logical operations only use register operands. Memory referencing is only allowed by load instructions.
Implementation artifacts hidden from machine-level programs. | Implementation artifacts exposed to machine-level programs.
Condition codes. | No condition codes.
Stack-intensive procedure linkage. | Register-intensive procedure linkage.

## Slide 11
RISC vs. CISC
CISC | RISC
Easy for compiler. | Need support of advanced compiler.
Fewer code bytes. | More code bytes.
More friendly to assembly code programmer. | Less friendly to assembly code programmer.
Currently dominates markets of PC processors and server processors | Currently dominates markets of embedded processors

## Slide 12
Processor Arch: Logic

## Slide 13
Logic Gates and Combinational Circuits
Outputs are Boolean functions of inputs
Respond continuously to changes in inputs
Continuously responds to changes on primary inputs
Primary outputs become (after some delay) Boolean functions of primary inputs

## Slide 14
Hardware Control Language (HCL)
HCL Examples:
bool eq = (a&&b)||(!a&&!b)
bool Eq = (A == B)
bool res = A in {item1, item2}
Bit-Level Multiplexor:
bool out = (s&&a)||(!s&&b)
Word Multiplexor:
int Out = [
s : A;
1 : B;
];
a, b, s: Bit-Level Representation
A, B: Word-Level Representation
HCL Word-Level Examples:

## Slide 15
Registers & Register Files
register
register
file

## Slide 16
Memories
data memory
instruction
memory

## Slide 17
Processor Arch: Sequential

## Slide 18
Basics
5 stages
  Fetch
  Decode
  Execute
  Memory
  Write back
  PC update
States
  PC
  CC
  Stat
  Register files
  Memories

## Slide 19
SEQ Hardware

## Slide 20
Opq, rrmovq, irmovq

## Slide 21
cmovXX

## Slide 22
rmmovq, mrmovq

## Slide 23
jXX, call, ret

## Slide 24
pushq, popq

## Slide 25
Fetch
HCL:

## Slide 26
Decode/Write back
HCL:

## Slide 27
Execute
HCL:

## Slide 28
Memory
HCL:

## Slide 29
New PC
HCL: