## Slide 1
TA：Wenhao Tang
ICS第六次小班课 11.12
MADE BY: Li zhuo & Wu Yiqian

## Slide 2: Contents
Memory Hierarchy
Cache Memories
Mid-term Review

## Slide 4: Memory Hierarchy
RAM
  SRAM v.s. DRAM
  DRAM:
    内存模块
    ➡️ DRAM芯片(多个，例如8个)
    ➡️ 超单元(d=r*c个)
    ➡️ DRAM单元(w个，通常w=8)
    ➡️ 1位
Bus structure – Memory Read/Write Transaction

## Slide 5: Memory Hierarchy
Random Access Memory(RAM)
  Volatile, compared to hard disk
StaticRAM v.s. DynamicRAM
  SRAM doesn’t need refresh
    faster and more expensive
    Used for cache memories
  DRAM
    Used for main memory

## Slide 6: Memory Hierarchy
Bus structure
Memory read transaction and write transaction through I/O bus
RAS & CAS
Notes: RAS和CAS共享地址线

## Slide 7: Memory Hierarchy
Disk:
Access Time: Seek + Rotation + Transfer

## Slide 8: Memory Hierarchy
SSD
  Sequential access faster than random access
  Writes slower than Read
    Modify a block page requires full page erasure and copy

## Slide 9: Memory Hierarchy

## Slide 10: Memory Hierarchy
Locality: Temporal and Spatial
Cache

## Slide 11: Cache Memories
Small, fast SRAM-based memories
Hold frequently accessed blocks of main memory
Cache hit
Cache miss

## Slide 12: Cache Memories

## Slide 13: Cache Memories
Direct Mapped Cache (E = 1)
  not match: old line replaced directly
Associative Cache(E > 1)
  One line in set is selected for eviction and replacement
  Replacement policies: random, least recently used (LRU), LFU
Fully Associative Cache(S = 1, E = C/B)
  search for many matching tags in parallel => expensive, should be small

## Slide 14: Cache Memories
Write-hit
  Write-through
  Write-back
Write-miss
  Write-allocate
  No-write-allocate
Write-through + No-write-allocate
Write-back + Write-allocate